Cleartides

Feeder 200, 500 and 2000.

The feeders should be mounted in the upright position on the side of the aquarium or sump.

There are two inlet feeds situated on the base of this feeder:

Hose One.

This is connected to an air pump and is controlled with the use of a control valve (included in kit x 2).

The use of a non-return valve is required if the air pump is sitting lower than the intake of the reactor.

Hose Two.

This is where the water intake is connected.

This is again controlled again with a control valve.

The feed of water can either come from a dedicated pump or from a feed off a main pump (this is done with the use of a reducing tee, ‘cut into’ the outlet of the main pump)

Water input into the Feeder is controlled by a control valve, which in turn controls the water exiting from the outlet of the Feeder. The water coming out of the Feeder, through the use of a 20mm tube, then runs water/ food into the aquarium or sump.

By controlling the water flow rate, you can control the amount ‘food’ the inhabitants receive over a period of time.